## Slide 1: MBIST Introduction
Viet Truong

## Slide 2: Agenda
Overview and definition
Why we use MBIST
Application
Reference

## Slide 3: Overview and definition
- MBIST (Memory built-in self test) is a mechanism of self-testing and repair for memory
- Extra circuits would be added around memories,
The circuit uses pattern shifted pattern from tester to execute testing and send response back.
- Tester observed analyzed pass/fail data from comparator

## Slide 4: Why is mbist used
Scan design/scan chain is not comprehensive to detect all memories’ faults due to difference in structure and memory function
MBIST provides self-repair mechanism and faulty cells analysis

## Slide 5: Build-in self repair
Soft-repair stores repair configuration in violate element (FF, scan register ...). BIST, BIRA and repair process must be executed every time the devide is power-up. Disavantages of this method is that unable to irritate hard corner in operation such as high voltage and temprature
Hard repair
  Laser-fused hard repair configure repair setting by laser-trimming which blows diffusion fuses but this requires extra manufactoring step to blow fuse and put the devide back to the tester.
  Electrical fuse repair doesn’t require extra manufactoring step, after BIST testing process, information from BISA tester determines properfuse to repair, the tester supply a programing voltage to blow the eFuse

## Slide 6: Logic build-in self test
To detect latent fault which may not apperant or detectable during manufactoring testing but may cause failure after a period of time under environmental conditions. Automotive and military applications in particular are worst affected.
  Need of performing routine tests on itself
  Doesn’t require tester, test vector can’t be control externally
  Cirtuitry is embeded in the chip(on-chip pattern generator, on-chip result compressor) that perform scan based structural test
  Test can be trigger by hardware everytime the device is on(offline testing) or application allows the test to run(online testing)

## Slide 7: Reference
https://www.einfochips.com/blog/memory-testing-an-insight-into-algorithms-and-self-repair-mechanism/
http://razzkamal.blogspot.com/2014/09/fuse-makes-repairable-memory-testing.html
https://static.aminer.org/pdf/PDF/000/282/891/dynamic_data_bit_memory_built_in_self_repair.pdf
https://vlsiuniverse.blogspot.com/2014/11/lbist.html
https://www.design-reuse.com/articles/38290/lbist-a-technique-for-infield-safety.html
https://www.design-reuse.com/articles/38290/lbist-a-technique-for-infield-safety.html

## Slide 9: Application
All type of memories: ROM, DRAM, SRAM, AsyncRAM